## Slide 1: Real-time systems
Using PLCs to implement
LADDER , Petri Nets and GRAFCET Diagrams

## Slide 2: Topics
The PLC (notion, architecture, working,…)
PLC programming languages (Ladder, IL, Grafcet)
Conversion between models
Exercises

## Slide 3: PLCs
http://machinedesign.com/engineering-essentials/engineering-essentials-what-programmable-logic-controller

## Slide 4: PLC definition
A PROGRAMMABLE LOGIC CONTROLLER (PLC) is an industrial computer control system that continuously monitors the state of input devices and makes decisions based upon a custom program to control the state of output devices.
Almost any production line, machine function, or process can be greatly enhanced using this type of control system. However, the biggest benefit in using a PLC is the ability to change and replicate the operation or process while collecting and communicating vital information.
Another advantage of a PLC system is that it is modular. That is, you can mix and match the types of Input and Output devices to best suit your application.

## Slide 5: Scan cycle
Four Steps In The PLC Operations
1) Input Scan
Detects the state of all input devices that are connected to the PLC
2) Program Scan
Executes the user created program logic
3) Output Scan
Energizes or de-energize all output devices that are connected to the PLC.
4) Housekeeping
This step includes communications with programming terminals, internal diagnostics, etc...

## Slide 6
Languages of the spacification standard IEC 61131-3 .
Por: Elton Ribeiro Matias
GRAFCET (Sequencial Function Chart - SFC)
Instruction List - IL
Ladder Diagrams - LD
Function Block Diagrams - FBD
Structured Text - ST
NETWORK 1
LD I0.0
A I0.1
= Q0.0
IL

## Slide 7: Our study will be based on the Siemens S7-200

## Slide 8: Structure of a S7-200 CPU

## Slide 9: Terminal diagram of the S7-200

## Slide 10: Connection to a computer

## Slide 11
Using a PLC

## Slide 12: Correspondence to original relay logic

## Slide 13
Working principle of PLCs
The S7-200 continuously cycles through the control logic in your program, reading and writing data. The S7-200 Relates Your Program to the Physical Inputs and Outputs :
Reading the inputs: The S7-200 copies the state of the physical inputs to the process-image input register.
Executing the control logic in the program: The S7-200 executes the instructions of the program and stores the values in the various
Processing any communications requests: The S7-200 performs any tasks required for communications.
Executing the CPU self-test diagnostics: The S7-200 ensures that the firmware, the program memory, and any expansion modules are working properly.
Writing to the outputs: The values stored in the process image output register are written to the physical outputs.

## Slide 14: The Logic is based on contacts

## Slide 15: Basic statements

## Slide 16: Structure of an operand

## Slide 17: “And” logic operation

## Slide 18: Current Flow in the Ladder Diagram

## Slide 19: “Or” Logic operation
The diagram expresses the following logic operations:
A0.0 = (E0.0 /\ E0.2) \/ E03
A0.1 = E0.1

## Slide 20: Making a standard “lock”
You are sure to be familiar with the standard latching function and here you will learn how to program it.
The example:
Output Q0.00 is to be activated as soon as S1 at input I0.0 is operated. With latching, Q0.0 is to remain active until S2 at input I0.1 is operated and thus interrupts the latch.

## Slide 21: Latching (retentive state)
To allow the latching function to work, the output (Q0.0 in this case), must itself ensure, as soon as it is activated, that it retains its "true" state and therefore remains active.
This is achieved by switching the output (Q0.0 in this case) as a contact in parallel to the tripping input just in the same way as with a conventional contactor circuit (Q0.0 can be compared to our contactor K1).
To allow the latching function to be terminated again, input I0.1 is to work like a break in the current path when operated.
If a current path is interrupted (i.e. state "0" exists) when a switch is operated, this is referred to as an NC contact.
Consequently, an element must be inserted which works as an NC contact in the ladder diagram when there are 24 V DC ("true") at input I0.1.X
Q0.0 as an input ensures latching

## Slide 22: Solution description and test

## Slide 23: A Different Take on Latching ... (1)
In PLC technology, latching is often also implemented in another variant:
Instead of feeding back the output - as in the previous example - here the functions "Set" and "Reset" are simply used instead..
Because of the "Set" operation - (S), a switching pulse at I0.0 has the effect that Q0.0 is activated in a steady state. In contrast, because of the "Reset“ operation - (R), a switching pulse at I0.1 has the effect that Q0.0 is deactivated again.
Number of bits next to Q0.0 that are set/reset.

## Slide 24: Edge detection (events)

## Slide 25: The pulse “contact”
The -|P|- and –N|- are provided for detecting rising and falling edges on the S7-200.
In the figure -|P|- works as follows:
The contact for detecting rising edges is closed for the duration of one cycle when the series connected contact changes from "untrue" to "true“.

## Slide 26: Pulse operated switch example

## Slide 27: Bit memories

## Slide 28: Bit memories utilization

## Slide 29: The process image input memory area

## Slide 30: Memory types
Bit memory: I0.0, V0.1, M1.3, …
Bytes: VB100, VB101, …
Words: VW: VW100, VW102, …
Doubles: VD100, VD103, …

## Slide 31: Timers
On-Delay Timer, Retentive On-Delay Timer, Off-Delay Timer.
The On-Delay Timer and Retentive On-Delay Timer instructions count time when the enabling input is ON. When the current value (Txxx) is greater than or equal to the preset time (PT), the timer bit is ON.
The On-Delay timer current value is cleared when the enabling input is OFF, while the current value of the Retentive On-Delay Timer is maintained when the input is OFF. You can use the Retentive On-Delay Timer to accumulate time for multiple periods of the input ON. A Reset instruction (R) is used to clear the current value of the Retentive On-Delay Timer.
Both the On-Delay Timer and the Retentive On-Delay Timers continue counting after the Preset is reached, and they stop counting at the maximum value of 32767.
The Off-Delay Timer is used to delay turning an output OFF for a fixed period of time after the input turns OFF. When the enabling input turns ON, the timer bit turns ON immediately, and the current value is set to 0. When the input turns OFF, the timer counts until the elapsed time reaches the preset time. When the preset is reached, the timer bit turns OFF and the current value stops counting. If the input is OFF for a time shorter than the preset value, the timer bit remains ON. The TOF instruction must see an ON to OFF transition to begin counting.

## Slide 32: Timer number and resolutions
You cannot share the same timer numbers for TOF and TON. For example, you
cannot have both a TON T32 and a TOF T32.

## Slide 33
Bits and words of timer identifiers
Timer Identifiers (T0,T1, …) can be used both as logic flags or as integer registers.
RUN timer_on_example.awl

## Slide 34: ON-delay timer diagram

## Slide 35: Timer on delay example
I0.0 activates Q0.0.
Q0.0 maintains its state (latch) since is also switched simultaneously in parallel with I0.0.
When T33 has elapsed, the latch function is broken via the T33 NC contact. Q0.0 goes off.
If T37 is not elapsed, the latch remains in force.
500*10ms = 5 seconds
RUN timer_on_example.awl

## Slide 36: Count up/down counters
The Count Up/Down instruction (CTUD) counts up each time the count up (CU) input makes the transition from off to on, and counts down each time the count down (CD) input makes the transition from off to on. The current value Cxx of the counter maintains the current count. The preset value PV is compared to the current value each time the counter instruction is executed.
Upon reaching maximum value (32,767), the next rising edge at the count up input causes the current count to wrap around to the minimum value (--32,768). On reaching the minimum value (--32,768), the next rising edge at the count down input causes the current count to wrap around to the maximum value (32,767).
When the current value Cxx is greater than or equal to the preset value PV, the counter bit Cxx turns on. Otherwise, the counter bit turns off. The counter is reset when the Reset (R) input turns on, or when the Reset instruction is executed. The CTUD counter stops counting when it reaches PV.

## Slide 37: Count Down instruction

## Slide 38: Count UP/Down instructions

## Slide 39
Counter down example

## Slide 40
The CTUD counter

## Slide 41: The CTUD example
Parts entering in a manufacturing assembling line are identified by a sensor connected to I0.0
Parts leaving the line are identified by a sensor connected to I0.1
If parts in the line are below 5, a light in Q0.0 must turn on.
If parts are between 5 and 9, turn on Q0.1
If parts are equal or above 10, turn on Q0.2
Integer comparison
Test the flag of the counter
CTUD_example.awl

## Slide 42
The Move, SUM and COMP instructins

## Slide 43
Instruction Lists (IL)
NETWORK 1
LD I0.0
A I0.1
= Q0.0
NOT
= Q0.1
NETWORK 2
LD I0.2
ON I0.3
= Q0.2
NETWORK 3
LD I0.4
LPS //Logical push stack
EU //edge up
S Q0.3, 1
= Q0.4
LPP //logical pop stack
ED //edge down
R Q0.3, 1
= Q0.5
Let’s try in Micro/Win

## Slide 44: Example 1
Translate these logic functions into corresponding LADDER diagrams:

## Slide 45: Solution
Translation of f1

## Slide 46: Resolution of example 1
Translation of f2

## Slide 47: GRAFCET
A denominação GRAFCET tem origem numa abreviatura francesa: Graphe Fonctionnel de Commande, Etapes Transitions (gráfico funcional de comandos estado transição).
O GRAFCET é um método gráfico de descrição do funcionamento da parte de comando de um automatismo concebido com o objectivo de permitir a simplificação da representação de processos complicados.
O GRAFCET, especialmente destinado para o controlo de máquinas e processos sequenciais, é comparável ao uso dos fluxogramas usados na programação de computadores.
Para o representar é utilizada uma sucessão alternada de ESTADOS ou ETAPAS e TRANSIÇÕES.
Um processo é decomposto em estados que serão activados sucessivamente.

## Slide 48: Sequences and convergence/divergences “and” “or”
Etapa inicial
Diverg. “ou”
conv. “ou”
Diverg. “e”
Conv. “e”
*
Etapa activa

## Slide 49
Grafcet: condições de transição de estado

## Slide 50
Grafcet: activação das saídas

## Slide 51: Ladder vs Grafcet

## Slide 52: Models translation
Conversion from … into …
  GRAFCET -> LADDER -> IL
  Petri nets -> LADDER -> IL

## Slide 53: Models conversion
Conversão Petri nets -> diagramas Ladder.
Conversão grafcet-> diagramas Ladder.

## Slide 54: Petri nets
Assumir que alguns “places” representam estados de sensores;
Assumir uma rede interpretada (acções associadas a transições e “places”);
Places P={p1,p2, p3, p4, p5}
Transitions T={t1,t2,t3,t4}
Inputs I(t1)={p1}
…
Outputs O(t1)={p2, p3, p5}
…
Marks mi=<1,0,1,0,2>
Capacity c=<2,1,3,1,4>
Availability Ai = c - mi =<1,1,2,1,2>
di =<0,0,0,0,0> delay (timed petri nets)

## Slide 55: Conversão “Petri Net” -> Diag. Ladder (generalized method)
Fazer marcação inicial.
Verificar se cada transição está habilitada (enabled), através de I(ti) e O(ti):
p  I : m(p) >=w(p, ti)
p  O: a(p) >=w(ti, p)
Fazer o disparo das regras habilitadas:
p  P : m’(p) = m(P) -w(p, ti)+w(ti, p)
(se w(x,y) não existir para uma dada transição, assumir zero).
Executar as acções semanticas às transições (incluíndo sensores)
Executar as acções semânticas associadas aos “places”.
I(t1)
O(t1)
(CONVERSÃO DEVERÁ SER FEITA POR SOFTWARE,
Following slides describe convertion for SAFE Petri Nets)

## Slide 56: Conversion example
System bit Sm0.1 is true only at the first CPU clock, then it remains false. It is useful for setting initial states.

## Slide 57: Conversion traffic_ligths

## Slide 58: Conflicting states (version 1)
This solution does not warrant only one transition fires

## Slide 59: Conflicting states (version 1) (prioritize transition T0)
This solution always favors transition To

## Slide 60: Exercise
Controlo de um semáforo de tráfego rodoviário
As luzes são: Q0.0: verde (30 seg.); Q0.1:amarelo (5 seg); Q0.2: Vermelho (40 seg);
O ciclo de trabalho inicia com I0.0 no estado 1.
T1
P1

## Slide 61: The Siemens Micro/Win software

## Slide 62: Installing Micro/win
Copy Microwin.exe from installation to the root of PC disck “c:\” (this is the license file, not a virus).
Try one of the provided installers which works in your windows version 7/8/10.

## Slide 63
Download a project

## Slide 64: Lab work
Petri Nets
LADDER/IL
Conversion Petri Nets -> LADDER
  MicroWin
  Simulador PLC S7-200
  Simulador estação de lavagem
  Utilização no PLC e Kit carwash

## Slide 65: The PLC simulator

## Slide 66: Simulador Estação Lavagem

## Slide 67: Kit car wash station
Let’s do it! 

## Slide 68: Accessing Help files of MicroWin
How to read an old “.hlp file” on Windows 10 (x64, or, x86)
How to read an old “.hlp file (*)” on Windows 10 (x64, or, x86) (*): The “.hlp file” must be read, without any problem, on Windows XP, 2000, ME, or, 98/98SE. The following is a procedure to be able to read an old “.hlp file” on Windows 10 (x86). (1) First, get the winhlp32.exe existing in the Windows directory of Windows XP (x86). (2) Make a temporary folder (for example D:\TEMP) on the HDD of Windows 10 (x86). (3) Copy the winhlp32.exe (obtained by the #(1) step) into the temporary folder D:\TEMP. (4) Make a file, named Win10-Hlp32-Fix.cmd, by using the text editor. All of the contents of the file (Win10-Hlp32-Fix.cmd) are as follows; @echo off set crtpth=%CD% takeown /f "%windir%\winhlp32.exe" >nul icacls "%windir%\winhlp32.exe" /grant *S-1-5-32-544:F >nul copy /y "%crtpth%\winhlp32.exe" %windir% icacls "%windir%\winhlp32.exe" /setowner "NT Service\TrustedInstaller" >nul echo. echo Done. echo. echo Press any key to Exit pause >nul exit (5) Therefore, you can find two files (winhlp32.exe and Win10-Hlp32-Fix.cmd) in the D:\TEMP. (6) Open the Command Prompt window, by selecting "Run as administrator.” (7) Then, move the prompt to the D:\TEMP directory, by using Change Directory (CD)command. (8) Under this condition, execute the Win10-Hlp32-Fix.cmd command in the D:\TEMP directory. (9) After the completion of this execution, you can read an old “.hlp file” on Windows 10 (x86). Remarks: In the case of Windows 10 (x64), please use the winhlp32.exe existing in the Windows directory of Windows XP (x64).
http://www.tenforums.com/general-discussion/16982-cant-read-older-hlp-files-windows-10-a.html